Assembly instructions SIDBlaster-USB Tic Tac

For the assembly, some experience in soldering is required. Under all circumstances, you’ll likely need:
- soldering station with a normal and a pointed soldering tip
- solder wire 0.7 and 1mm
- working lamp with magnifier
- flux pen
- hand suction pump
- tweezers
- small side cutter
- small flat or needle nose pliers
- isopropyl alcohol or denatured alcohol
- brush or toothbrush
- meter
- wooden toothpick
Assembly Steps:
Owners of a kit with a pre-assembled SMD part start at point 16.
1. equip FT232 chip (U2); the following pin numbers must be soldered up: 1; 4; 5; 7; 12; 14; 15; 16; 17; 18; 20; 21; 23; 25.
   hint: subsequently check the right connections according to the circuit diagram with a multimeter ("wiring test")
   Please note: For correct operation, pin 26 must be switched on mass. This was forgotten in the layout of revision 1.2. Therefore, bridge pin 25 with pin 26. This is fixed from revision 1.3
2. equip LEDs D2: blue; D3: red; consider mark!
3. equip R1 and R2, 270 Ohms
4. equip C1, 10nFs
5. equip U4, Imprint: B6287G; attention! U4 is turned by 180° in relation to U2
6. equip C3, C4, C2, C21, C5, C6, C7, C20, C12(from Rev. 1.4): 100nFs
7. equip R23 (18k)
8. equip R22 (47k)
9. equip R20 und R21 (1k)
10. solder on inductor (L2), tip: tin-plate pads in advance
11. solder diode D1 (SS26)
12. Q1 (from Rev. 1.4) equip
13. Equip R3, R4 (from Rev. 1.4) 1K
14. Equip R5 (from Rev. 1.4) 10K
15. clean circuit-board
16. equip USB jack socket
17. equip L1
18. C10, C11 (22uFs), C13 (4,7µF)(from Rev 1.4) consider polarity
19. test: connect current source, blue LED must be on; measure voltage between pin 14 (GND) and pin 28 (+12V) of U3 (SID)
20. equip JP1 (Red)
21. Test: set JP1 and mesure voltage at the SID socket (must be 9V now)
22. solder on U1, pinch off spare ends
23. IC socket for SID: cut connections with side cutter, sand smooth
24. solder in the two parts of the socket
25. flash FT232 template: software tool "FT_Prog" by FTDI required. Connect circuit board, start FT Prog, scan for device, load template (GitHub), right click on Device ->Apply Template. Then click "program" and program. Attantion! New template for Rev. 1.4!
26. flash PIC µC: A programming device like PicIt 3 is needed, possibly build adapter cable (see manual), software: MPLAB IPE. Kit customers receive a pre-programmed PIC.
27. Test: Connect the board and start ACID 64 Player (Version 3.6.3; copy hardsid.dll (32Bit) to the same folder beforehand), play a tune, SIDBlaster should be recognized and the red (green) LED will flicker.
  Note: It is best to equip 2 groups per blue (JP2&3) and green (JP4&5) pin strip with the associated capacitors and solder them together, otherwise holes could become clogged. If the holes get blocked, use a suction pump and toothpick.
  2. Note: It is best to always solder strips and components to one pin first, so you have the convenient opportunity to correct the fit again.
28. equip JP2-JP6
29. equip SV1 and SV2
30. equip C70, C71 (470pFs)
31. equip C72, C73 (22nFs)
32. equip C80, C81 (1800pFs)
33. equip C82, C83 (2,2nFs)
34. equip R12, R8 (1K)
35. equip R14, R9 (10K)
36. equip C18 (1000pFs)
37. equip C8, C9 (100nFs)
38. set jumper JP1: red; JP4 & JP5: green; JP2 & JP3: blue; JP6: white
39. Equip T1, observe polarity according to data sheet! (May deviate from the equipment label!) With Rev.1.2 a PN2222A must be fitted the wrong way round, from Rev.1.3 the equipment label is right for PN2222A
40. equip C77, C79 (10uFs, bipolar), polarity irrelevant
41. solder on jack sockets
42. Clean the circuit board with a toothbrush and spirit and let it dry. I personally get the best results with denatured alcohol.
43. measure voltages again
44. install SID
45. check jumper
46. connect to personal computer and test with ACID player (Version 3.6.3, see above).